## Slide 1: POWER TRADE AGREEMENT
Sher singh bhat

## Slide 2: POWER TRADE AGREEMENT IS OUR NEED RATHER THAN CHOICE

## Slide 3: TYPICAL FLOW DURATION CURVE AND DESIGN PLANT CAPACITY
Chart: 
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100
Series 1 | 66 | 52 | 45 | 37 | 33 | 27 | 18 | 13 | 11 | 8 | 7 | 6 | 5.5 | 5 | 4.5 | 4.3 | 3.7 | 3.5 | 3 | 2.7 | 2.1
Column1
Column2
M^3/S
% OF TIME
Firm power 5 MW
Installed capacity at Q65: 12 MW
Installed capacity at Q40: 20 MW
Installed capacity at Q25: 35 MW

## Slide 4
Q (P)
3Q/3P
Import
Diesel
Storage
July
December
June
SEASONAL SURPLUS AND DEFICITS DUE TO TYPICAL FLOW DURATION CURVE

## Slide 5: Balance 2018/19 considering Under Construction
Particulars | Hydro | Thermal | Others | Total
Existing capacity | 722 | 53 |  | 775
Capacity addition |  |  |  | 
NEA | 136 |  |  | 
NEA Subsidiary and associate companies | 725 |  |  | 
Other IPPs | 296 |  |  | 
Total ongoing augmentation | 1157 | 150 (imp) |  | 1307
Altogether in 2018/19 | 1879 | 203 |  | 2082
Demand | Peak 1907 |  | Off peak 1050 | 
Wet Season Balance | Neck to neck |  | About 1000 MW surplus 20 hrs. a day | 
Dry season | Available 750 Deficit 1200 MW |  | Deficit 400 MW Load shed > 10 hrs. | 

## Slide 6: IN BRIEF
Wet Season after 3-4 years
  Huge off peak surplus worth 20 BNR; if not marketed in X- Border market total loss to NEA
  Poor product so price may be too low even if marketed
  In both cases loss will have to be recovered by increasing tariff
Dry Season after 3-4 years
  Large deficit and load shedding if not imported in large volume
  Current import worth 10 BNR, might go 25 BNR in 2018/19; Electricity import second highest
So Power Trade Agreement with India is our NEED to:
  Market the Seasonal Surplus to keep down the effective retail tariff
  To import during deficit dry months and eliminate load shedding
  To harness hydro-potential and market power
  Otherwise only 2000 MW capacity in 2018/19 has become problem, what about 83000 MW.

## Slide 7: X-BORDER TRADING OF ELECTRICITY (IN INDIAN MARKET)

## Slide 8: TRADING OF ELECTRICITY IS TYPICAL
Unlike other commodities, Trading of electricity needs special markets
  It is intangible commodity
  It cannot be stored and has to be consumed at the moment it is generated
  It needs a hard wire connection from generation to point of consumption
  It is not measurable at the custom point

## Slide 9: INDIAN POWER SECTOR AND MARKET
CSGS
SGS
IPP LONG TERM PPA
IPP under Bidding
Private Merchant
Renewables
Long term Bilateral
Short term Traders
DAM IEX/PXIL
UI
Public DISCOMS
Private DISCOMS
Large consumers
Public
Private
Joint Projects

## Slide 10: DERIVED NEPALESE WISH LIST FOR PTA (1)
Area | Issue | Analysis
Development of hydropower | PTA should have provisions to accelerate not regulate | 
 | No outside intervention on how and when to develop Nepal’s hydropower | 
 | No provision acceptable that eclipses Nepal’s water right on its territory, right on added value of water during the course of hydropower development | 
Domestic Requirements | PTA to ensure that export of electricity shall be only after meeting Nepal’s domestic requirement in REAL TIME | 
Accessibility in Indian Market | PTA to ensure market for all generated power for design optimization at best use | 
 | PTA should provide non- discriminatory access to Nepalese public and private generators in Indian market and transmission grid | 
 | All tariff and non- tariff barriers on import/ export of electricity to be waived. | 
 | Nepalese power to have access in all kinds of Indian markets ( Long term, short term and spot market) | 
 | No direct or indirect special tariffs or special clearances on importable power in India | 
Tariff | PTA should ensure best market prices above cost of generation | 
 | Product value of peak and off peak power be ensured | 
 | Respective parties should be allowed to sign PPA in INR, USD or NR as per their mutual convenience | 

## Slide 11: DERIVED NEPALESE WISH LIST FOR PTA (2)
Area | Issue | Analytic note
Market coupling | Perfect integration as common market but Nepalese consumers should not be exposed to catastrophic price hike in common market due to supply deficits. If Nepal is entering long term market, Nepal’s export will not entertain market price hikes but Nepalese consumers will be exposed to it. So Nepalese consumers should be immunized from it. (How it will be done? Insulate domestic market? Then integration will be of different kind.) | 
Risks | No risk of marketing in volume as well as in cost of generation | 
 | PTA should not expose Nepal to FOREX Risk | 
Net off gain to GON | PTA should ensure definite predefined net off gain to GON on per unit of exported energy considering the concessions and incentives offered by the GON for development of hydropower. | 
Third Country Sale | PTA should allow export of power by Nepal to a third country using Indian grid | 

## Slide 12: NEPALESE WISH MARKET
N
MM
INDIAN
MARKET
Bhutan
Bangladesh
Sri Lanka
Pakistan
Maldives
NEPAL
INDIA

## Slide 13: DERIVED INDIAN WISH LIST FOR PTA
Area | Issue
Development of hydropower | India wishes to be involved in the planning and development of hydropower in Nepal through cooperation agreement
 | It will ensure the planning and development of domestic transmission system in Nepal, X-Border transmission system and expansion and reinforcement of Indian transmission system
 | Indian public/private entities should get preference in development of hydropower in Nepal.
Market access | Entry of Nepalese power in Indian market should be step wise in regulated volumes so that it is not detrimental to the Indian market and put the investments in India at risk.
 | Large volume of Nepalese power should enter Indian market through a single window instead of mushroomed numerous parties in Nepal getting direct entry
 | Nepalese power should enter the long term market through single window and this single window in India then take it to the Indian market on market portfolio basis
 | No direct or indirect special tariffs on exportable power by Nepal (royalty and permission for export)
Pricing | Nepalese power should enter the long term market at cost of generation
 | Joint group for estimation of cost of generation price at which power will enter into India.
 | In case Nepal needs to import, it should purchase it from short term Indian market
Third country sale | No direct export through Indian transmission system, it enters India through single window, becomes Indian power, enters Indian market and then may go to Bangladesh as Indian power from market

## Slide 14: INDIAN WISH MARKET
MM
MARKET
Cost of generation transaction
Through Nodal Agencies
Transaction through market
Bhutan
Nepal
Bangladesh
Sri Lanka
Pakistan
Maldives
India

## Slide 15: NEPAL POSITION
Generation sector
  Public sector generator(s) for domestic requirements with seasonal surplus and deficits
  Private generators of small and medium size
  Large private generators directly targeting export market
  P2P Cooperation projects conceived for future
All of these want access to Indian market by their own
  No country will allow such unplanned energy access
  Every country has its own energy security concerns
The kind of PTA we conclude will guide the financing of projects
  We might have very good market accessibility but not suitable for financing
  Kind of wish list we have, asks merchant plants. Can we get them financed?
  Can we afford the volume and price risks of short term market?
  Can we ensure transmission for large volume of export in short term market?
Very clear
  Hydropower marketing doesn’t go that way (like potatoes).
  It has to go very much planned. Mostly it is long term market based.
  Most important is “ Wish lists of two sides should not be mutually exclusive, but complimentary.”
  If it did not happen for last many years, will not happen for further many years if we don’t compliment.

## Slide 16: WHAT CAN WORK?
Short term and
spot market
GATE 1:
Long term guaranteed market
Price and volume guaranteed
Guided by co-operation Agreement
Financing not a Problem
Integration of:
Any private
GATE 2:
Long term market ( bid or bilateral
Price regulated by CERC, and volume not guaranteed
Any private direct
Any public direct
GATE 3:
Short term or Spot market
( nothing guaranteed)
Integrated surplus of public sector
P2P
Nepali Public Sector
Individual Private sector direct
Indian Public Sector

## Slide 17: MARKET ACCESSIBILITY GATES
Domestic or Indian public sector
p2p
private
Integrated real time surplus
Long term
Short term
Spot mkt.
UI
GATE 1
Individual Private/public
Byer DISCOM or large Consumer
GATE 2
GATE 3

## Slide 18: GATES
GATE NO. | GATE TYPE | PURPOSE | OTHER DETAILS
1 | Gate for Toll Road | Long Term, P2P, Pre-Fixed Tariff | Indian, Nepalese or any other developers may use this gate through single Nodal agency but no direct entry of individual developers
2 | Gate for Common Road | Long Term, public/private, Purchase and price through bilateral negotiation or bidding, Price regulation may be applicable | Any public or private developer can use this gate for direct entry into Indian Market
3 | Gate for track for two wheelers | Short term or Day ahead spot market | Individual public or private developers will gave entry in short term market through traders or can have membership in spot market i.e. Energy Exchanges
4 | Gate for Transit passengers | Third country sale using each others network | Without entering in the electricity market
PTA shall ensure PRINCIPLE OF RECIPROCITY for all gates.

## Slide 19: REVIEW OF PTA DOCUMENTS
PTA Signed in 1996: A good will document only
PTA proposed by Nepal in 2010: “Dhoka Khol (Open the Gate)!!” document
PTA proposed by India in 2014: “ Trade in Co-operation Frame” document
Required: 4-Gate document

## Slide 20: WHY DOESN’T IT HAPPEN? THE NEXUS
INVESTORS NEPAL’S HYDRO POTENTIAL MARKET
N
Nepali public/private sector
Indian public sector
Other Foreign Investors
International Financers
Manufacturer’s Agents
Project Facilitation brokers
Indian private sector
Indian Power Traders
Pressure Groups
PTA
PCA
BANGLADESH
INDIA
PTA
This time India mixed PCA with PTA in the same document so that if you hit PCA, PTA will be hit automatically.

## Slide 21: AGREEMENT
Article 1: Grid Interconnections and Power Trading
1.1 This Agreement will enable export and import of electric power between Nepal and India on mutually acceptable terms or
as provisioned in this Agreement.
1.2 The Parties agree to take steps to establish suitable grid connectivity between the two countries. The Parties agree to
develop a coordinated procedure for secure and reliable operation of the national grids joined by cross border
transmission interconnections and to prepare scheduling, dispatch, energy accounting, settlement and procedures for
cross border trade of electricity.
1.3 Subject to necessary approvals, the Parties agree to provide non- discriminatory access to the cross border
interconnections or to their domestic transmission systems for all participants of the common electricity market or
national markets of the Parties.
1.4 Both Parties agree to establish cooperation on a bilateral and/or multilateral basis on the various aspects of
development of harmonious policy on the realization of cross – border interconnections and power trade.
1.5 Subject to necessary approvals, both Parties will endeavor to allow the licensed electricity traders of each country to and
to operate in the other country and to engage in cross –border electricity trading and to seek transmission access for this
purpose in cross-border or domestic transmission systems.

## Slide 22: AGREEMENT
Article 2: Access to Market
2.1 Both Parties will endeavor to remove all kinds of tariff and non-tariff barriers in the trading of electricity including
but not limited to doing away with the requirement of licensing and taxes/duties in the cross border exchange of
electricity.
2.2 Both parties agree to acknowledge and register all public or private generators, transmission providers, distribution
and supply service providers, large consumers and traders of each other’s countries as participant entities in their
respective national markets or common market of electricity provided such entities wish to take membership in such
market under the extant policies.
2.3 The market participants as under Article 2.2 may apply for and shall get non-discriminatory market access to any
market they wish; including but not limited to long term, short term, day ahead and renewable markets in each
other’s national market or in common market.
Article 3: Investments and development of power sector
Both Parties agree that Parties may independently develop their own power sector including but not limited to
generation and transmission of electricity according to their plan through public or private investments from any
sources.

## Slide 23: AGREEMENT
Article 4: Co-operation in the field of Power
4.1 The parties agree that they wish to enhance their co-operation in the field of power including investments for mutual benefit. In furtherance thereof, the Parties agree to encourage and facilitate joint co-operation in following areas:
  Co-operation in power generation and transmission
  Co-operation for the development of human resources through trainings for consulting and other related services, energy efficiency and for research and development.
4.2 The Parties shall encourage and facilitate investments in each other’s country in the field of electricity generation and transmission.
4.3 The Parties shall co-operate in effective harnessing of Nepal’s hydropower potential through facilitation and speedy construction of hydropower projects in Nepal by joint venture investments of Nepalese public sector with Indian public sector in the mutually agreed investment proportion. The parties agree to develop up to 10,000 MW of electricity and associated transmission system by 2025 through such joint venture projects irrespective of hydropower projects through other public or private investments.
4.4 Both Parties agree that Power from such joint projects developed under cooperation shall be exported only after meeting Nepal’s real time requirement.
4.5 Parties shall identify the projects for development through joint venture as under Article 4.3 and sign a Project Implementation and Power Purchase Agreement (PIPPA) for each individual project. Notwithstanding anything written in this Agreement and extant policies in the countries of the parties, including tariff principles, PIPPA shall prevail.
4.6 Parties shall develop a template of PIPPA and tariff calculation principle applicable for all such projects to be developed under Article 4.3.

## Slide 24: AGREEMENT
Article 5: Institutional Arrangement
5.1 Joint Steering Committee: JSC shall be co-chaired by Power Secretaries of the two countries
  JSC shall review overall status of power trade between the two countries, ongoing developments and future perspectives. It will also review the progress of Joint Venture Projects as well as different working groups and nodal agencies constituted as under this Agreement
  JSC shall meet at least once a year at mutually agreed venue
5.2 Joint Working Group: JWG shall be comprised of experts of two sides as nominated by the parties.
  JWG shall promote and facilitate all aspects of power trade between the two countries as envisioned in this Agreement.
  JWG shall promote and facilitate the co-operation between the Parties as envisioned in this Agreement
  JWG shall meet twice a year at mutually agreed venue
5.3 Joint Technical Sub-Committee for System coupling
5.4 Joint Sub-committee for Market Coupling
5.5 Nepal Nodal Agency (NNA):
  for management of power sale to Indian Nodal agency regarding the generation from JV projects
  For management of sale of integrated surplus of Nepalese public sector
5.6 Indian Nodal Agency (INA)
  For management of marketing of power supplied by NNA from JV projects
  For management of marketing of surplus of Nepalese public sector available through NNA

## Slide 25: AGREEMENT
Article 6: Sale of Electricity to Third Country
Both Parties agree to provide non-discriminatory access to each other in their transmission system for sale of electricity to any third country.
Article 7: Term
Term of this Agreement shall be ---- years and may be reviewed/renewed/ renewed with review after ------ years.
Article7: Save and Repeal
All existing arrangements between the Parties shall remain in place.

## Slide 26: THANKS